TEXAS INSTRUMENTS (TM) - 990 MINICOMPUTER - DX10 KERMIT (TM)

     Author: Paul W. Madaus
     Johnson Controls, Inc. M-66
     507 E. Michigan St.
     Milwaukee, WI  53201
     (414) 274-4528

     PLEASE READ THE LAST PAGE OF THIS DOCUMENT  BEFORE  CONTINUING.   This
     version of KERMIT was written for  the  TI-990 family of minicomputers
     running the DX10 operating system.  The KERMIT source used for this TI
     version originated from a  version  of  KERMIT  designed to run on the
     Sperry(UNIVAC) 1100.   I  chose  to  convert  this  version  of KERMIT
     because of its  heavy  use  of  standard  Pascal.    Before continuing
     further, I wish to credit the  base  of this TI version of KERMIT(i.e.
     the Univac Pascal source code) to:

     Edgar Butt               (LAST KNOWN ADDRESS)
     Computer Science Center
     University of Maryland
     College Park, Maryland 20742
     Phone (301) 454-2946

     The TI version of KERMIT, referenced  herein  as  KERMIT,  was written
     under  DX10  O/S  Rel.  3.7.0.    The  program  was  written  using TI
     Pascal(TIP) Rel. 1.8.0.    TIP is a superset of standard Pascal.  Some
     TIP procedures were used within KERMIT, especially  SVC$ for low level
     I/O.  The program also consists of one external procedure,  written in
     TI-990 assembly language, called SETPDT.  The TI  Pascal Configuration
     processor(program  splitter)  was  not  used  for portability reasons,
     however a  user  may split the program into modules and use XCONFIG if
     one so desires.

     KERMIT can be initiated from  a  VDT931,  VDT940  or  VDT911 terminal;
     other devices  have  not  been tested but may also work.  The included
     SCI(DX10  System Command Interpreter) procedure is used to bid or call
     the KERMIT task, and may have  to  be  modified  to  fit  a particular
     system's environment.   The  KERMIT  port(i.e. remote port to modem or
     remote system) is generated into the system using XGEN.  The following
     device   configuration   was   extracted   from   a  .S$SYSGEN.<system
     name>.CONFIG file and shows how I generated  the  KERMIT  port into my
     system.

     DEVICE TYPE? VDT             STxx
     ACCESS TYPE? RECORD
     TIMEOUT? 0
     CHARACTER QUEUE? 128
     VDT TYPE? 931
     ASSOCIATED PRINTER? NO
     SWITCHED LINE? NO
     SPEED? 1200
     INTERFACE TYPE? CI403
     TILINE ADDRESS? >F860
     CHANNEL NUMBER? 0
     INTERRUPT? 11



                                    Page  1







     I was able to  gain  the  most  functionality by using the 931 DSR and
     CI403 interface  board.    The PASSTHRU mode(ref. DX10 O/S Application
     Programming Guide Vol. 3, Jan. 85, p. 9-38) of the  931 DSR is used to
     control  echo   and   special   character   problems   by allowing the
     application to gain direct control  of the terminal.  A KSRDSR and EIA
     card were initially  tested  with  KERMIT,  but  extremely limited the
     functionality of KERMIT to packet  transfer and one-way login.  A user
     may implement other hardware configurations, but will probably have to
     make some program changes  within  the  procedures    INITIO, CONNECT,
     PRSCMD, and other procedures that use or are PASSTHRU  dependent.  The
     above CHARACTER QUEUE,  and  INTERRUPT  LEVEL  may  be  fine  tuned as
     necessary.    I  have  successfully tested KERMIT at 4800 & 9600 bauds
     with an IBM-PC (TM) to TI-990 direct  connection,  but  recommend 1200
     baud to start with.  The remote port(CI-403/931DSR)  defaults to 7-bit
     data  and  odd  parity.    It  is  possible  to  dynamically set these
     parameters on the CI-403 board from a user task(KERMIT), however I did
     not have time to put these enhancements into KERMIT.  Therefore, users
     will have difficulty talking to other  systems whose ports are not set
     at 7-bit  data  and  odd  parity,  with  the  TI-990 as the initiating
     system.  The cables used for remote connections  from  the CI-403 port
     are:

     TI Part No. 2303070-0003   to modem - straight thru signal connections
     (i.e. TD-TD, RCV-RCV etc.)

     TI Part No. 2303077-0001  direct connect -  (signals  are TD-RCV, RCV-
     TD, RTS&CTS-DCD etc.)

     Homemade cables with the minimum RS-232  signals  work  fine.   An ISC
     type terminal is mentioned both  in the KERMIT program and the bidding
     SCI procedure.  This terminal type setting is  required  if your local
     console  terminal is uppercase only, its DSR does not support PASSTHRU
     mode, you cannot  suppress  echo,  or  some  other  unusual support is
     needed.  The setting of an ISC terminal type is left as an expert mode
     prompt in the bidding SCI procedure; of  course this may be changed as
     needed.  Opening the TI-990 port locally for  connection  to  a remote
     system(or modem) fails due to some port initialization problems.  This
     problem  forced  me  to actually set two terminal init bits within the
     remote port device's PDT, if the  SVC(low-level  I/O) open fails.  See
     the procedure SETPDT  for  more  information  on  this.    It would be
     advisable for the  system  administrator  to  hardcode the remote port
     name into the calling  SCI  procedure as a safeguard against modifying
     other 931 PDT's.  Since software checks do exist(see procedure CHKTRM)
     to prevent  this, my main concern is to avoid the frustration that may
     exist from a user not knowing the KERMIT remote port name.

     All commands entered within  KERMIT  should  be  uppercase  only.  The
     program can be easily modified to handle lowercase commands if needed.
     It  is  only  necessary  to  enter  the  first  three  characters of a
     command,although full  file  pathnames must be used where appropriate.
     KERMIT does not support  the use of synonyms within filenames that are
     entered in any of the  commands  at  this  point  in  time.  Type HELP
     within KERMIT  to  view  a  list  and  brief  syntax  of the following
     supported commands.




                                    Page  2







     LOG <OPTIONAL FILENAME>  -  Set logging within KERMIT.  A filename may
     be entered, or use the default filename  .KERLOGxx  where  xx  are the
     digits of the user's console terminal number.  The name of the default
     filename may be adjusted  within the bidding SCI procedure - parameter
     number 5.   Send  and  receive  packets,  reads  and writes to a file,
     remote port and  console  terminal  I/O  errors, problems in receiving
     packets, send file sizes, remote  port  character  overflows, framing,
     and parity errors, setting and resetting of XON and XOFF, and entering
     server mode are all items that are logged when logging is enabled.

     CONNECT  -  Connect to the remote port.  This command is only valid in
     local mode and will connect your console terminal via the local KERMIT
     port to whatever is connected  to  your  remote  port(e.g.  modem, PC,
     direct  system  connect).   Once connected, type two  @  (at signs) in
     quick sequence to return to your  local  KERMIT  command  mode.  Other
     special character sequences are allowed for  the  ISC  terminal, since
     the non-PASSTHRU capability  of  this  terminal inhibits the user from
     entering  important  keys  such  as  CMD,  BLNK-ORNG, or DC1.  If your
     console is  an  ISC terminal, then these special key sequences will be
     displayed  to  your  console upon connect.  Once connected to a remote
     system, a user may logon to that system, bring up and place the remote
     KERMIT into  a  server mode, and then escape back to your local system
     to initiate file transfers.  It is the user's responsibility to logoff
     a remote system, via BYE, FINISH and reconnect, etc.

     SEND <LOCAL  FILE>  <OPTIONAL REM FILE>  -  Send a file from the local
     TI-990 system  to  some  remote  system.  The local filename must be a
     full legal DX10 filename, no synonyms as  previously  mentioned.   The
     optional remote filename can be entered in any  shape  or form that is
     legal to the remote system(where the file is being sent).  If a remote
     filename  is  NOT  entered,  then  the  local  filename(without parent
     directories)  is  extracted  from  the  local pathname and used as the
     remote name.  It  is recommended that only sequential files be sent to
     another  system.    Other  file  types(e.g.  relative record, KIF-does
     anybody use these??) may not produce consistent results.

     RECEIVE <DX10 RECEIVE FILE NAME>  -   Receive  a  file  from  a remote
     system and  place  it  into  the  RECEIVE  FILE NAME.  RECEIVE is like
     putting  your TI-990 KERMIT into a server mode for only one file.  The
     file  to be received must be sent using the send command from a remote
     system.  KERMIT returns to the command mode after a file is received.

     FINISH  -   SHUT DOWN the remote KERMIT or at least take it out of the
     server mode, depending on how the remote system handles  this command.
     I've seen it perform both of  the  above  operations.    If  issued to
     another TI-990 system running this version of KERMIT, then the command
     will both end the server  mode AND the KERMIT task.  The user can then
     expect to connect to SCI upon connecting back to a TI-990 remote.

     BYE   -   SAME as above, but also log off the remote system.  If a TI-
     990 KERMIT receives the BYE command while in server mode,  it will set
     a special synonym to be checked by the  bidding  SCI  procedure.   The
     bidding SCI procedure will check  the  value  of  this  synonym before
     exiting and either invoke the DX10 Q(quit) command to log the user off
     the system if BYE was received or return the user to SCI.



                                    Page  3







     TEST  -  Place the TI-990 KERMIT into a send  only test mode.  Packets
     are  sent  from  KERMIT  obeying   all   state   rules,   however,  NO
     acknowledging packets from a  remote  system  are received.  This mode
     can  be  used  in conjunction with logging(see LOG) to see exactly how
     KERMIT is building and sending its packets.   Once the TEST command is
     set,  a  user   must   exit   and   re-enter   KERMIT to resume normal
     transmissions(i.e. you can  not  reset  the  TEST comnmand).  The TEST
     command will only test the commands SEND, FINISH and BYE.

     EXIT  -  EXIT KERMIT and return to SCI.    If  used locally, it is the
     user's responsibility to shut  down  and/or  log off any remote KERMIT
     that may still be running.

     SERVER  -  Place  KERMIT  in  a server mode.  Once in the server mode,
     KERMIT will accept  various commands(GET, BYE, FINISH, SEND) from your
     local  machine.  If a serving KERMIT is inactive, it will periodically
     send NAKs to your local machine to keep things from hanging(e.g. PCs).
     A serving KERMIT  must  be  ended  by either receiving a BYE or FINISH
     command.

     BINARY  -  SEND/RECEIVE a binary type file.    If  receiving  a binary
     file, it is advised that  you let KERMIT create the (new)file for you.
     If  sending  a binary file, the file must have a logical record length
     of 80 bytes.   Binary data exists on TI most often as compiler object,
     assembler object, compressed linked  object,  or  backup directory(BD)
     data.    The  first  three items above are structured by default in 80
     byte records.  Backup  directory  files,  which  can be used to handle
     most  if  not  all  DX10  file types,  can be moved from one system to
     another using KERMIT if blocked at 80 byte records.  If you block a BD
     at 80 bytes, and let BD create a file for you, the BD file will adhere
     to the  80 record size limitations.  KERMIT may blank fill records for
     you if they are less than 80 byte records.   This  proved  to be of no
     problem for  the  types of binary files described above.  Obviously, I
     do  not  consider  moving  binary  data  as  critical  as  moving text
     data(i.e. source  files),  and  likewise  only  covered the basics for
     binary file transfer.

     TEXT  -  SEND/RECEIVE TEXT FILE data.    This mode of file transfer is
     the  default  for  KERMIT.   However, users may switch while in KERMIT
     from binary mode to text mode using this command.

     GET <REMOTE FILE NAME> <LOCAL FILE>  -    GET a file(REMOTE FILE NAME)
     from a remote  KERMIT  that is in the server mode, and place that file
     in LOCAL FILE.  Unlike most  KERMITs,  GET does not prompt you for the
     names  of  the  remote   and   local   filenames.    In addition, both
     filenames(remote & local) must be entered.  The remote filename may be
     any lowercase(e.g. UNIX (TM)) or uppercase filename  that  is legal to
     the remote system.  The local name must be a full legal DX10 pathname.

     HELP  -  Display the list of TI-990 KERMIT supported commands.








                                    Page  4







     KERMIT may be compiled using the  standard  TI  XTIP command.  Some of
     the options listed below may not be standard as supplied by TI.


     XTIP (EXECUTE TI PASCAL COMPILER <VERSION: 1.8.0 83357>)=2,
     SOURCE = <KERMIT source>
     OBJECT = <KERMIT object>
     LISTING =<KERMIT compiler listing>
     MESSAGES = ME  <or some other name>
     OPTIONS  =  FGND,FIN,GLOBALS,MAP,GLOBALOPT,NOL/P=255    <  or whatever
     suits you>
     MEM1 = <default>
     MEM2 = <default>
     MEM3 = 10,0          <note stack reduction for extra heap needed>


     The SETPDT assembly language file must then be assembled using XMA.


     To link KERMIT use the standard XLE command.


     XLE (EXECUTE LINKAGE EDITOR) =2,
     CONTROL ACCESS NAME = <control file as listed below>
     LINKED OUTPUT ACCESS NAME = <a program file>
     LISTING ACCESS NAME = <link edit listing>
     PRINT WIDTH = <default>
     PAGE LENGTH = <default>
     MODE(F,B) = <either F or B>


     The link edit control file that I used is:


     FORMAT     IMAGE,REPLACE,4
     LIBRARY    .SCI990.S$OBJECT
     LIBRARY    .TIP.OBJ
     TASK       KERMIT
     INCLUDE    (MAIN)
     INCLUDE    <filename of compiled KERMIT object code>
     INCLUDE    <filename of assembled SETPDT object code>
     INCLUDE    .TIP.MISC.ACCDXO
       <used for TIFORMS clearscreen - may be omitted>
       <if procedure declarations taken out of source>
       <see procedure declarations in source file.>
     END

     After successful compilation, assembly and linking,  perform  a Modify
     Task Entry(MTE) to make the KERMIT task priviledged.  The priority may
     be moved up here also, if you wish.

     After  installing  the  KERMIT proc(SCI procedure) onto an appropriate
     proc library(e.g. .S$PROC), type the  proc  KERMIT to initiate KERMIT,
     assumming that the proper hardware connections have been made.




                                    Page  5







     KNOWN AREAS FOR IMPROVEMENTS

     1. The connect procedure is probably the greatest.  In trying to avoid
     any assembly language,  the connect procedure became very complex, and
     is suseptable to losing characters to mention the least.

     2. If  TI-990  KERMIT  is  acting  as a server, and you type something
     wrong on a  remote  machine,  you may lose state synchronization.  You
     may have to  type  the  command  over  about  four  times  to  get the
     server(TI-990) back in sync.

     3. Use of synonyms in DX10 filenames.

     4. Lowercase as well as uppercase command support.

     5. User setting of baud, parity and data  word  size - a capability of
     the CI-403.

     6. Logging  in  TI  from  some  other  system  may require special 931
     emulation.  If  you  can  put up with the garbage characters until you
     actually get into TI KERMIT then you'll be OK.

     7. Switching back and forth from  binary  to  text  or  text to binary
     modes may cause problems.

     8. VT-100 emulation.

     9. and whatever other bugs that you may find.






























                                    Page  6







     Recompiled and  relinked TI-KERMIT on March 16, 1987.  Then tested TI-
     KERMIT with an IBM-PC XT running  MS-KERMIT  2.29.    On  the  TI side
     successfully tested: SEND,  GET,  FINISH, CONNECT-did a CTTY on PC and
     ran "limited" MS-DOS  (TM)  commands  on  the  TI-911VDT and LOG.  The
     following list of TI-KERMIT connections have worked in the past:

         a. TI-990 and TI-990
         b. TI-990 and PC(PC means either IBM-XT, TI-PC, TI-Portable
            or COMPAQ)
         c. TI-990 and TI Explorer
         d. TI-990 and TI-Nu Machine (running UNIX).

     However,  these  TI-KERMIT  connections  have not been tested recently
     (except  for  the  IBM-PC)  and  the  current  working status of these
     connections is UNKNOWN.











































                                    Page  7







     ONE FINAL NOTE:

     Unfortunately, yet a reality most of us experience,  my  other project
     work, my  school  work,  and  most  importantly  my  family  life have
     prevented me from completing,  to  my  expectations,  this  version of
     KERMIT.  This version has successfully transferred data between TI-990
     systems and UNIX machines, PCs or other TI systems - using both direct
     connect and modem communications, but still contains many bugs.   Once
     a data transfer is initiated, you can expect the  process  to complete
     with very good reliability.  Bugs  mainly  exist  within  the areas of
     connection and state transition (between  commands).    The writer and
     Johnson Controls, Inc.  is NOT liable for the use of this software, or
     for any effects caused by the use of this software.  Anyone using this
     software is using it at their own risk.  Any use of this software must
     comply  with  all  rules,  regulations  and  copyrights that have been
     established by Columbia University.   It  is the user's responsibility
     to obtain,  to  read  and  to  understand  all  KERMIT regulations and
     stipulations set forth by Columbia University.


     TM - TRADEMARKS

     TEXAS INSTRUMENTS  IS  A  REGISTERED  TRADEMARK  OF  TEXAS INSTRUMENTS
     INCORPORATED.

     KERMIT IS A REGISTERED TRADEMARK OF HENSON ASSOCIATES, INC.
     (Creators of The Muppet Show)

     IBM IS  A  REGISTERED  TRADEMARK  OF  INTERNATIONAL  BUSINESS MACHINES
     CORPORATION.

     UNIX IS A TRADEMARK OF AT&T.

     MS-DOS IS A REGISTERED TRADEMARK OF MICROSOFT CORPORATION.
























                                    Page  8