## Slide 1: 15th Annual Tcl/Tk Conference October 2008
Timothy L. Tomkinson
Fellow Software Engineer
Northrop Grumman Electronic Systems
Remote Control of Test Equipment Using Distributed Objects
Notes: <number>

## Slide 2: Agenda
My Background
Problem: Controlling Complex Test Stands
  Communication between network nodes
  Hardware control
Networking Solutions
  Custom middleware
  Off-the-shelf solution using CORBA
  Tcl solution using distributed objects
Hardware Control
  Tcl and Ffidl
Example
Conclusion
<number>
Notes: <number>

## Slide 3: My Background
Education
  B.S. Electrical Engineering: Carnegie Mellon University
  M.S. Computer Science: Johns Hopkins University
Air Force: 5 years
  Satellite Software Engineer
  DMSP: Weather Satellites
Northrop Grumman: 14 years
  Embedded, real-time software
    VxWorks
    VME, CompactPCI
    C/C++
  Test Software
    Windows, Unix, VxWorks
    Ethernet, GPIB, RS-232, 1553, USB
    Tcl, C/C++, SQL
Tcl User: 10 years
<number>
Notes: <number>

## Slide 4: Typical Test Stand
<number>
Database
GPIB
USB
VME
CompactPCI
RS-232
Control PC
Ethernet
1553
Operator PC
PCI
Notes: <number>

## Slide 5: Custom Middleware
Create custom client/server applications
Need to know network programming on different platforms
  Steep learning curve on some platforms/languages
Need to define network protocol and message structures
  Separate code required to encapsulate and extract messages
  Tedious to maintain
Expensive
<number>
# Power Supply Message
typedef struct
{
MessageId msgId;
PowerSupplyId psId;
float voltage;
} PowerSupplyMsg;
X
Notes: <number>

## Slide 6: CORBA
Common Object Request Broker Architecture
Platform-independent infrastructure for communicating over a network
Messages are defined using a generic Interface Definition Language (IDL)
IDL compiler generates client and server objects
Client object used to connect to server object and execute remote method calls
Method arguments, return values, and exceptions are encapsulated and extracted automatically according to IDL
ORB (Object Request Broker) provides main event loop processing and message dispatching
Complicated/expensive
<number>
Notes: <number>

## Slide 7: CORBA Architecture
Interface
Definition
(IDL)
IDL Compiler
Client (Operator PC)
Server (Control PC)
Implementation
Class
Skeleton
Class
ORB
<number>
ORB
Stub
Class
Network
Notes: <number>

## Slide 8: Tcl Distributed Objects
Client (Operator PC)
Server (Control PC)
<number>
Network
“Remote”
Class
Local
Object
Target
Object
“Remote”
Class
“Remote” class manages infrastructure
Target object created on server
Introspection used to generate local object
Local methods and procedures replaced with remote method calls
Operations on local object transparently executed on target object
Notes: <number>

## Slide 9: Advantages
No IDL compiler
  Client and server objects created at runtime from single Itcl class
  Same language on both ends
  Introspection
No ORB
  Network communication managed by “comm” package
  Message dispatching managed by Tcl interpreter
  Event loop managed by Tcl event loop
Transparency
  Itcl class does not need to be modified to run remotely
  Other than startup code, client app is not aware that local object is running remotely
<number>
Notes: <number>

## Slide 10: Hardware Control
“Ffidl” package used to call shared libraries
  Foreign Function Interface with Dynamic Loading
  Tcl extension on top of either “libffi” or “fficall”
  Creates Tcl commands that map to functions in shared libraries
    DLLs (Windows) or shared objects (Unix)
    Custom or COTS
    Examples: Win32, NI-VISA, 1553, VME, PCI, etc.
  Eliminates need to write Tcl extensions
  Ported to VxWorks
    Uses VxWorks symbol table
    Allows direct calls to kernel and user modules
Wrapper class created for each library to provide object-oriented interface
<number>
Notes: <number>

## Slide 11: Hardware Control (cont’d)
Device
Driver
Ffidl
Shared
Library
Device
<number>
Test
Script
Library
Wrapper
Test scripts written in procedural Tcl
Device drivers written in object-oriented Tcl
Library wrappers provide OO interface to shared libraries
Ffidl acts as bridge between Tcl and C
Shared libraries: DLLs or shared objects, custom or COTS
Hardware device
Notes: <number>

## Slide 12: Device Driver Classes
Command table contains method names vs. command strings
Initialization code creates public methods for each command
Public methods call the same private method to write to device
Same concept used for query commands
<number>
class PowerSupply {
package require NiVisa ;# library wrapper
# Command table (method vs. command string)
foreach {method cmdStr} {
reset *RST
voltage VOLT
...
} {
# Create write methods
public method $method {args} \
“eval handleWrite $cmdStr {$args}”
}
# Write to device
private method handleWrite {args} {
$niVisa write $args
}
}
# Example
$ps reset
$ps voltage 5.0
Notes: <number>

## Slide 13: Example
<number>
Server side
    # Start the server
    package require Remote
    Remote::config –port 5000 –local 0
Client side
    # Create instance of “Remote” object
    package require Remote
    set remote [Remote #auto $hostname 5000]
    # Use “send” method to load package
    $remote send “package require PowerSupply”
    # Use “new” method to create object
    set ps [$remote new PowerSupply]
    # Call methods
    $ps reset
    $ps voltage 5.0
Notes: <number>

## Slide 14: Conclusion
CORBA paradigm very easy to implement in Tcl
  Itcl provides all necessary object-oriented extensions
  Tcl’s introspection facility eliminates need for interface definition file
  Comm package provides robust remote procedure calls
Ffidl is perfect for controlling hardware
  Easy to call C libraries without writing Tcl extensions
  Can use existing device drivers, either COTS or custom
Tcl’s portability allows seamless control across multiple platforms
Distributed object architecture provides rapid development
  Code can be tested and debugged on local PC
  To deploy, only a few extra lines are required to run remotely
  No knowledge of network programming is required
  Since code does not need to be modified, any Itcl object can be run remotely
Fast, simple, inexpensive
<number>
Notes: <number>

## Slide 15
<number>
Notes: <number>